SAFETY SECTION

# WARNING!!!

Do not use Yellowjack unless you completely understand how it works and are familiar with tower safety procedures.

Avoid tower work during inclement weather. Wind, rain, snow, hail, ice and other wet weather conditions will make the tower slippery and create a risk of serious injury or death.  Use of the Yellowjack while doing tower repair in wind, thunderstorms, lightning, and other weather conditions creates a serious risk of injury or death.

Always use safety lanyard while using Yellowjack.  Do not hoist yellowjack to working height without a lanyard, and always secure it to tower.  Make others aware of the possiblility of falling objects.

Lanyard is NOT designed or rated for your personal safety, only to hold the tool from falling.  Do not use it on your fall arrest harness or to hold climber to the tower.

Power lines can kill you. Look up before you go up.  Don’t work under power lines or with any object that can come in contact with a power line, i.e., antennas, poles, ladders, etc.   Contact with power lines can result in serious injury or death.

Fall danger:  ALWAYS wear fall arrest harness when working on a tower.  Failure to use or properly attach a harness can result in serious injury or death.

Always have a helper with you when doing tower work.  This is both for safety and convenience.  Make the helper aware of the possibility of falling objects.

Working at heights: If you are not comfortable working at heights, get professional help.  When working at heights always work in plenty of light and dry conditions with a harness.  Failure to maintain balance and have proper safety harness can result in serious injury and death.

The buyer understands the above potential hazards of using the Yellowjack and working at heights, as well as other that may arise without warning, and holds manufacturer harmless for any and all claims that may arise out of the use or installation of the product, whether for injury or damage to property of any kind including antenna towers and damage or injury to any third party.

# Yellowjack Instructions

Yellowjack allows for easy removal and assembly of Rohn tower sections.  IT is made to fit on Rohn 20, 25g, 45g, and 55g.  (The leg alignment end of the tool will not fit on Rohn 55g, but will assemble and disassemble sections.)

Ball pin:  Use ball pin to keep both rotating bars from moving when hoisting Yellowjack to working height, for storage, or to keep one end from rotating when using the opposite end.  Wrap cable around engagement bar to secure it.  Leg alignment bar is secured by swivelling it backwards and inserting pin through both holes.

Note that it is possible to put too much force on tower rungs with this tool, deforming them in the process.  Be careful and watch what you are doing.  Use tool a little at a time around each side of the tower so tower section is removed evenly.

# Disassembling Tower Sections

Yellowjack can be used to push stuck tower sections apart.  After bolts are removed from all three legs, position Yellowjack as shown below.  Push up on end of tool to “lever” sections apart.  It may be necessary to “ratchet” the tool into another engagement bar slot to continue pushing tower sections apart.  The above procedure should be followed near each tower leg, going around the tower multiple times to get stubborn sections apart.  Note:  It is also possible to position Yellowjack upside down as compared with below photos.  This would change the upward motion on the end of the tool to a downward motion.

# Assembling Tower Sections

Yellowjack can be used to pull tower legs together.  Always test fit sections on the ground before trying to do it in the air!  Mark each section so they can be assembled in the air in the same order and same alignment as test fitting on the ground.

Place Yellowjack on tower as seen below. Tower rung should be placed in engagement bar slots that are facing up.  Pull handle down to bring sections together.  It may be necessary to “ratchet” the engagement bar by repositioning it in a different slot to get a new purchase, then continue bringing sections together until fully joined.

# Aligning Tower Legs

Yellowjack can be used to align a bent or off axis leg.  First, secure engagement bar with ball pin cable.  Position alignment end of tool as shown below.  Pulling on handle can leverage leg into alignment with opposite leg.  It may be necessary to have a helper pull upper leg onto lower one while using tool.  When all three legs are fitted together, use tool as described above to fully assemble tower sections.

Before each use, check the following:

- Hardware:  Make sure both bolts and nuts are present and tight on Yellowjack.

- Use ball pin to secure engagement and alignment bars so they don’t pinch or clobber you while hoisting tool to operating height.

- Look for bends, deformities, cracks, or missing parts on tool.

- Check lanyard for frays, cuts, or seperations.  Check carabiners for cracks, bends, etc.  Do not use if these conditions are present!  Toss it and get a new lanyard.  WARNING!  Lanyard is not a personal safety device!  Do not use it on safety harness or as a safety line!

If any of these conditions are present correct or repair before use.

Thanks for your purchase.  Please call with questions.

KF7Pmetalwerks

3641 So. 700 W.

Salt Lake City, UT 84119

    - Chris@KF7P.com

# Text boxes

Leg

Push up on handle to push sections apart.

Pull handle down to bring sections together.

READ THIS MANUAL BEFORE USING THIS PRODUCT.  Failure to follow the instructions and safety precautions in this manual can result in serious injury or death.  Keep this manual in a safe location for future reference when using this product.

Loop for lanyard or carabiner

Ball pin

Engagement bar

Leg alignment bar